## Slide 1: Hardware Cache Coherence
Write-back caches (rather than write-through) for performance reasons
Coherence Controller (CC)
  Monitors (“snoops”) bus traffic (addresses and data)
  Executes the coherence protocol
    What to do the with local copy when you see different things happening on bus
Three core-initiated events
  Ld: load St: store WB: write-back
Two remote-initiated (bus) events
  LdMiss: read miss from another core
  StMiss: write miss from another core
Core
D$ data
D$ tags
CC
Bus

## Slide 2: VI (MI) coherence protocol
VI (valid-invalid) protocol: aka MI
  Two states (per block in cache)
    V (valid): have block
    I (invalid): don’t have block
    Can implement with one bit (the valid bit)
Protocol diagram (left)
  If anyone else wants to read/write block
    Give it up: transition to I state
  WriteBack (WB) if your own copy is dirty
This is an invalidate protocol
Update protocol: copy data (write-through), don’t invalidate
  Sounds good, but wastes a lot of bus bandwidth
I
V
Load, Store
LdMiss (Send Data), StMiss, WB
Load, Store
LdMiss/ StMiss

## Slide 3: VI Protocol State Transition Table
 | From This Core |  | From Other Cores | 
State | Load | Store | Load Miss | Store Miss
Invalid (I) | Miss  V | Miss  V | --- | ---
Valid (V) | Hit | Hit | Send Data  I |  I
Rows are “states” (I vs V) of data blocks in the caches
Columns are “events” in the cores
  WriteBack events not shown
  V  I on a LdMiss also updates memory (Send Data) if block is Dirty
Memory sends data when no core responds

## Slide 4: Example of VI Snooping Protocol
Core 1
Core 2
L1 I$
L1 D$
L1 I$
L1 D$
Shared Memory

## Slide 5: Example of VI Snooping Protocol
Core 1
Core 2
L1 I$
L1 D$
L1 I$
L1 D$
Shared Memory
X = 0
Load X
X = 0
Load X
X = 0
Store 1 to X
X = I
X = 1
When the second miss by Core 2 occurs, Core 1 responds with the data value for Core 2 (canceling the response from the shared memory), updating the value of X in the shared memory, and invalidating its own copy
LdMiss seen by Core 1, so Core 1 invalidates its copy
StMiss seen by Core 2, so Core 2 invalidates its copy
X = 1
X = I
Load X
LdMiss seen by Core 1, so Core 1 does a Send Data and then invalidates its copy
X = I
X = 1

## Slide 6: VI  MSI
VI protocol is inefficient
  Only one cached copy allowed in entire system
    Multiple caches copies can’t exist even if they are all read-only
MSI (modified-shared-invalid)
  Fixes problem: splits “V” state into two states
    M (modified): local dirty copy
    S (shared): local clean copy
    I (invalid)
    Takes 2 bits to implement
  Allows either
    Multiple read-only copies (S-state) --OR--
    Single read/write copy (M-state)
I
M
Store
StMiss, WB
Load, Store
S
Store (UpgMiss)
Load, LdMiss
LdMiss (Send Data)
StMiss
Load
LdMiss/ StMiss

## Slide 7: MSI protocol state transition table
 | From This Core |  | From Other Cores | 
State | Load | Store | Load Miss | Store Miss
Invalid (I) | Miss  S | Miss  M | --- | ---
Shared (S) | Hit | Upg Miss  M | --- |  I
Modified (M) | Hit | Hit | Send Data  S | Send Data  I
M S transition on a LdMiss also updates memory (Sends Data) since the block is Dirty

## Slide 8: Example of MSI Snooping Protocol
Core 1
Core 2
L1 I$
L1 D$
L1 I$
L1 D$
Shared Memory
X = 0
Load X
X = 0S
Load X
X = 0S
Store 1 to X
When the second miss by Core 2 occurs, Core 1 responds with the value canceling the response from the shared memory (and also updating the value of X in the shared memory and marking its own copy as shared)
LdMiss seen by Core 1 (no action required)
StMiss (UpgMiss) seen by Core 2 so Core 2 invalidates its copy
X =1M
X = I
Load X
LdMiss seen by Core 1, so Core 1 does a Send Data of X and marks its copy as shared
X = 1
X =1S
X =1S
Core 1 marks X as modified and sends out an UpgMiss